# BOP.BAS.115 Passenger briefing
Regulation (EU) 2018/395
The pilot-in-command shall ensure that before and, when appropriate, during the flight passengers are given a briefing on normal, abnormal and emergency procedures.
## AMC1 BOP.BAS.115 Passenger briefing
ED Decision 2018/004/R
General
1. Passengers should be given a verbal briefing and demonstration about safety matters in such a way that the information is easily retained and applied during the landing and in the case of an emergency situation.
2. The briefing/demonstration should include the following items:
  1. safety in relation to ground equipment;
  2. use of internal handholds;
  3. wearing of suitable clothing;
  4. smoking regulations;
  5. in-flight use and stowage of personal belongings and baggage;
  6. importance to remain inside the basket at all times, particularly after landing;
  7. landing positions to be assumed to minimise the effect of the impact during landing;
  8. safe manoeuvring of the balloon on the ground after landing;
  9. use of oxygen-dispensing equipment, if applicable; and
  10. other emergency equipment provided for individual passenger use, if applicable.
3. Part or all of the verbal briefing may be provided additionally by a safety briefing card on which pictorial instructions indicate the correct landing position.
4. Before take-off, the correct landing position should be demonstrated.
5. Before commencing the landing phase, passengers should be required to practise the correct landing position.
### GM1 BOP.BAS.115 Passenger briefing
ED Decision 2018/004/R
General
The pilot-in-command or a person designated by the operator is carrying out the passenger briefing.
BOP.BAS.120 Carriage of special categories of passengers