# CS 31HB.23 Load factors
ED Decision 2009/005/R
1. Flight load factor. In determining limit loads, the limit load factor must be at least 1.4, except for (b).
2. Landing load factor. For all parts belonging to the balloon’s suspension system, including the envelope to suspension system pick up points, limit load must be determined using a limit load factor of at least 3.0.
→ CS 31HB.25