# CS 31HB.63 Occupant restraint
ED Decision 2009/005/R
1. There must be a restraining means for all occupants, which can take the form of hand holds. (See CS 31HB.59(h))
2. For baskets having a separate pilot compartment, there must be a suitable restraint for the pilot which must meet the strength requirements of CS 31HB.30. Additionally, the restraint must be designed so that:
  1. the pilot can reach all the necessary controls when the restraint is correctly worn and adjusted;
  2. there is a method of quick release that is simple and obvious; and
  3. the possibility of inadvertent release is minimised.
# AMC 31HB.63(a) Occupant restraint
ED Decision 2009/005/R
Note: Operational legislation may also require pilot restraint to be fitted to balloons which have a single compartment basket.
→ CS 31HB.67